## Slide 1
ENGINEERING DESIGN 2026
Individual Checkpoint
Work package briefing — what's due, from whom, and what “good” looks like
DUE FRIDAY 11 SEPTEMBER 2026
North-West University | School of Electrical, Electronic and Computer Engineering | Second Semester

## Slide 2
EEII – I
Drive Electronics
PROTECTION IS MANDATORY
Checkpoint task
Level-1 simulation of the 3-phase bridge inverter using ideal voltage-controlled switches — SPWM switching logic, correct 120°-spaced 3-phase output.
Using the same ideal-switch model, simulate three fault conditions: shoot-through, an output phase-to-phase short, and an overload.
Model at least one candidate protection mechanism (input fuse/current limit, overcurrent trip, relay bus disconnect) and show its effect on each fault.
No hardware yet at this checkpoint — the milled half-bridge protection board is a separate, later build.
BRING THIS
Simulation schematic (ideal switches)
3-phase line voltage plots, 120° spacing confirmed
Fault current waveforms — with and without protection, for all three faults
Short memo: recommended protection strategy — trip thresholds and disconnect timing
Individual Checkpoint · due 11 September 2026 · rolled I1 + I2 individual grade (20%)

## Slide 3
EEII – II
Magnetic Load Attachment
NO COTS ELECTROMAGNET
Checkpoint task
Build a 2D axisymmetric finite-element model of the 3-point solenoid electromagnet in FEMM.
Extract pull force on a steel plate as a function of coil current, at the expected operating air gap.
Derive a preliminary coil specification from the force curve — the starting point for winding later.
COTS core material is permitted; a complete pre-made electromagnet or solenoid is not.
BRING THIS
FEMM model file, geometry and materials documented
Force-vs-current curve at operating air gap
Preliminary coil spec: turns, wire gauge, expected resistance and current at target force
Individual Checkpoint · due 11 September 2026 · rolled I1 + I2 individual grade (20%)

## Slide 4
REII
Remote Control Dashboard
MUST USE NRF24L01
Checkpoint task
Bring up a live nRF24L01 link on an existing dev board / breadboard — not the from-scratch STM32F411 ground-station dongle yet.
Characterise the link systematically: packet loss vs. distance, at a minimum of two data rates.
Identify the best channel for the lab environment — account for WiFi and other groups' simultaneous links.
This proves the radio itself is reliable before the full dongle build and protocol design are committed to.
BRING THIS
Packet-loss vs. distance curves, ≥ 2 data rates
Channel selection with interference analysis
Recommended nRF24 configuration — channel, data rate, power, retry settings
Individual Checkpoint · due 11 September 2026 · rolled I1 + I2 individual grade (20%)

## Slide 5
MCTR – I
Lateral Movement
MOTOR COST < R250
Checkpoint task
Manufacture an initial wheel arrangement from the curated pre-printed wheel sets (varied, internally logged print parameters).
Measure static and kinetic friction / traction force at the operating load.
Test a minimum of two wheel configurations and compare.
Derive the motor torque requirement at the wheel from the measured results.
BRING THIS
Measured static & kinetic traction forces at operating load
Comparison of ≥ 2 wheel configurations, with material justification
Calculated motor torque requirement feeding gearbox/motor selection
Individual Checkpoint · due 11 September 2026 · rolled I1 + I2 individual grade (20%)

## Slide 6
MCTR – II
Spooling
NO WORM GEARBOX
Checkpoint task
Run a gear stage on the converged gear test rig (quasi-static stall test, module-5, printed-on-printed).
Characterise mesh quality, backlash, and load capacity against the rig's known failure modes.
Load cell integration and calibration are deferred to Increment 3 — not part of this checkpoint.
Findings carry directly into the multi-stage (≥ 2 stage) gearbox built in I3.
BRING THIS
Printed gear pair, tooth geometry & print parameters documented
Measured backlash and load-test result
Note: load cell explicitly deferred — flag as provisional in the ICD, not omitted
Individual Checkpoint · due 11 September 2026 · rolled I1 + I2 individual grade (20%)

## Slide 7
THE CONTROLLER
Bulk Reference — What's Fixed, What You Own
SUPPLIED TO EVERY GROUP
CORE BOARD
lecturer-supplied · every group
ESP32-S3-WROOM-1 N8R2 · 3.3V LDO · native USB · ADS1220 24-bit SPI ADC · microSD (SPI) telemetry log · WS2812 status LED · EN/GND reset
↔
IO BOARD
student-built, perfboard · owner: EE2 or MC2 (TBD)
nRF24L01 radio · opto-isolation on EE1×6, EE2 magnet PWM, MC2 dir/PWM · MC2 quadrature encoder in · 5-pin expansion header · bench-verify isolation before live EE1 gate drivers
↔
GROUND STATION
CE deliverable, end to end
STM32F411 USB dongle · native USB + nRF24 driver, no scaffolding · bridges radio ↔ PC dashboard
Firmware model
No CE student: pre-compiled ESP32 binary, UDP over built-in WiFi — works standalone, zero extra build
With CE student: ESP32 source w/ nRF24 driver stubbed in; STM32 dongle fully open (bring-up + driver + USB)
Control philosophy
Real-time loop — drive signals, sensor reads, interlocks — runs ON the ESP32, never on the PC
nRF24 not fit for tight feedback; core crane function is independent of dashboard/CE availability
Anti-sway & obstacle avoidance: open-loop, model-based — no IMU, no obstacle sensor needed
GPIO / pin budget
26 committed of 34 usable GPIO (36 total − 2 for native USB)
6× EE1 gate/PWM · EE2 magnet PWM · MC2 dir/PWM/encoder×2 · nRF24 CS/CE/IRQ · SPI×3 · 5-pin expansion
8 pins margin remain — 4 free, 4 strapping-reserved
OPEN — RESOLVE BEFORE THE ICD IS DRAFTED
IO board owner: EE2 or MC2 · core/IO board schematics not yet finalised · analog signal conditioning for magnet current-sense is the IO board's job, unspecified
Controller Specification 2026 · reference for all five work packages and the group ICD

## Slide 8
KEY DATES
What happens next
11 Sep
Individual checkpoint due — all five work packages
14 Sep
Increment 3 begins — group ICD drafted & signed off in week 1
27 Oct
Participation marks captured
13 Nov
Final Demonstration
16 Nov
Final Group Presentation & Individual Portfolio
North-West University · Engineering Design 2026 · full schedule: EngDesign2026_Revised_Timeline.docx